## Slide 1
How to
Add Door Station to NVR for Preview and Playback – Via Web
Add Device to NVR
Go to Device Access > Device > Access Control Device, click Add and enter door station information to add door station, click Save.
The NVR firmware version should be 5.04.050 or above.
Set Recording Schedule
Go to Storage Management > Storage Schedule > Video Recording, set the schedule, click save.
2
3
1
2
3
4
When add successfully, you can find device status is online, you can also turn to Live View to confirm the live view is normal.
1
2
1
2
3
Go to Playback, choose the channel, you can slide the time bar to check the playback video.
3
1
2
Here we take iDS-7716NXI-M4/X and DS-KD8003-IME1(B) as an example.